Turbine Temperature Comparison Chart

DISPLAY CHARACTERISTICS

|  | TT1000A | TT1200A |
| --- | --- | --- |
| 3.5 digit digital display | S | - |
| 4.5 digit digital display | - | S |
| Temperature simulation/measurement in °C | S | S |
| Temperature simulation/measurement in mV | - | S |

SYSTEM LEAD RESISTANCE COMPATABILITY

|  | TT1000A | TT1200A |
| --- | --- | --- |
| All lead resistance systems, except 16 ohm | S | S |

MEASUREMENT RANGE AND RESOLUTION

|  | TT1000A | TT1200A |
| --- | --- | --- |
| Resistance to 200 ohms | S | - |
| Resistance to 20k ohms | - | S |
| Highest resistance resolution is 0.01 ohms | S | - |
| Highest resistance resolution is 0.001 ohms | - | S |
| Insulation to 2 megohms | S | - |
| Insulation to 200 megohms | - | S |
| Highest insulation resolution is 100 ohms | - | S |
| Certified temperature range to 1000°C | S | - |
| Certified temperature range to 1300°C | - | S |
| Temperature resolution 1°C | S | S |
| Temperature resolution 0.1°C | - | S |

ACCURACY

|  | TT1000A | TT1200A |
| --- | --- | --- |
| Resistance accuracy of ± 0.1% ±0.1 ohm | S | - |
| Resistance accuracy of ± 0.05% ±2 counts | - | S |
| Insulation accuracy of ± 3% of reading ±1k ohm | S | - |
| Insulation accuracy of ± 5% of reading ±2 counts | - | S |
| Temperature measure accuracy of ± 1°C | S | - |
| Temperature measure accuracy of ± 0.5°C | - | S |

OPTIONS AND OTHER FEATURES

|  |  |  | TT1000A | TT1200A |
| --- | --- | --- | --- | --- |
| Can be used as a master indicator |  | S | S |
| Automatic cold junction compensation |  | S | S |
| Battery Access Without Disassembly |  | - | S |
| GE CF6-80 series adapter |  |  | O | O |
| GE CF6-6, -50 series adapter |  | O | O |
| Millivoltage doubled system adapter cable |  | - | O |
| S = Standard Feature | O = Option | - = Not | available |  |

Barfield Inc.

4101 NW 29th Street.

Miami, Fl. 33142

Phone Line: (305) 894-5400

Fax Line: (305) 894-5401

AIRCRAFT MAINTENANCE REPAIR OVERHAUL & SUPPORT