City of Roanoke

Public Works Service Center

Standard Operating Procedure

Subject: Storm Filter Inspection & Maintenance

Revised: 9/27/19

Purpose: To ensure proper inspection and maintenance is performed

Responsible Party/ies: Stormwater Field Operations Supervisor

Performance Frequency: Every six months the Storm Filter will be cleaned per manufacturer standards.

Documentation: Storm Filter Inspection Report and Storm Filter Maintenance Report (both attached). Completed reports will be kept on file in Division’s records and a copy emailed to envmgmt@roanokeva.gov.

Training: The Stormwater Field Operations Supervisor will cover this SOP with all newly hired and/or temporary personnel within their first 60-days of employment if their duties and responsibilities include the maintenance or inspection of the storm filter.

Trainees must complete the signature section below and a copy of the signed SOP shall be sent to Environmental Management.

Procedure:

- Every six months: Stormwater staff shall inspect, clean and maintain the Storm Filter per the manufacturer standards.

- Complete the Storm Filter Inspection Report form, follow the fields to guide the inspection and record the necessary information.

- If maintenance is needed, complete the Storm Filter Maintenance Report form to guide the inspection and record the necessary information.

- Return the completed Report Form(s) to the Stormwater Division office. Scan and e-mail a copy of the completed form(s) to Environmental Management at: envmgmt@roanokeva.gov.

Trainee Name:	________ Signature:  ____________________________

Date Trained: ________________________

Send completed form to Environmental Management at: envmgmt@roanokeva.gov.

Annual Storm Filter Inspection Report Log

Storm Filter Inspection Report

| Date: |  |  |  |  | Inspector: |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Location: |  |  |  |  | System Size: |  |  |  |  |  |  |  |  |
| System Type: Vault |  | Cast-In-Place |  |  | Linear Catch Basin |  | Manhole |  | Other |  |  |

Sediment Depth on Vault Floor: ________________

Structural Damage: __________________________

Estimated Flow from Drainage Pipes (if available):__________________________________________

| Cartridges Submerged: Yes | No |  |  |  |  |  | Depth of Standing Water: |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Storm Filter Maintenance Activities (check off if done and give description) |  |  |
| Trash and Debris Removal: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Minor Structural Repairs: |  |  |  |  |  |  |  |  |  | __ |  |  |  |
| Drainage Area Report: |  |  |  |  |  |  |  |  |  |  |  | __ |  |  |  |
| Excessive Oil Loading: |  | Yes ____ | No ____ | Source: ________________________ |  |  |
| Sediment Accumulation on Pavement: | Yes ___ | No ____ _ | Source: __________________________ |  |  |
| Erosion of Landscaped Areas: |  | Yes ____ | No | __ | Source: |  |  |
| Items Needing Further Work: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Owners should contact the Storm Water Division (853-5900) and inquire about how the department disposes of their street waste residuals.

Other Comments:

Send completed form to Environmental Management at: envmgmt@roanokeva.gov.

Storm Filter Maintenance Report

| Date: |  |  |  |  | Inspector: |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Location: |  |  |  |  | System Size: |  |  |  |  |  |  |  |
| System Type: Vault |  | Cast-In-Place |  |  | Linear Catch Basin |  | Manhole |  | Other | ___ |

List Safety Procedures and Equipment Used:

System Observations:

Months in Service:

Oil in Forebay (if present):  Yes	No

Sediment Depth in Forebay (if present): __________________________________________________

Sediment Depth on Vault Floor: ________________________________________________________

Structural Damage:

| Drainage Area Report |  |
| --- | --- |
| Excessive Oil Loading: Yes ____ No | Source: _________________________________ |
| Sediment Accumulation on Pavement: Yes ____ | No _____ Source: ___________________________ |

Erosion of Landscaped Areas:  Yes _____ No _____ Source: _________________________________

Storm Filter Cartridge Replacement Maintenance Activities

| Remove Trash and Debris: | Yes |  |  | No |  | Details: |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Replace Cartridges: Yes |  |  | No _____ | Details: __________________________________________ |
| Sediment Removed: Yes |  |  | No _____ | Details: __________________________________________ |

Quantity of Sediment Removed (estimate?): ________________________________________________

Minor Structural Repairs:  Yes _____	No ______ Details: ____________________________________

Residual (debris, sediment) Disposal Methods and Comments:

____________________________________________________________________________________

____________________________________________________________________________________

Send completed form to Environmental Management at: envmgmt@roanokeva.gov.