TOWN OF BETHLEHEM - Continuous Deflective Separation (CDS) Unit Maintenance Inspection	REPORT FORM

Instructions: Use this form to record inspection and maintenance activities associated with the CDS Unit then submit an electronic copy to the Town SITE INFORMATION

|  | Facility Owner: |  |  |  |  |  |  |  |  | Facility Address: |  |  |  |  |  | Unit ID #: |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Inspector Name: |  |  |  |  |  |  |  |  | Type of Inspection: | Storm Event / Monthly / Quarterly / Annual | CDS Model: |  |  |
|  | INSPECTION NOTES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Inspection Items |  |  | Inspector Comments |  | Observed Field Conditions Indicating | Corrective Action for Maintenance Performed | Corrective |
|  | (Inspection Criteria) |  |  |  |  | Maintenance is needed for the Unit |  | Action Date |
|  | Exterior of CDS unit |  |  |  |  |  | Malfunction or damage to cover or apron | Repair or replace identified exterior component |  |
|  | (Exterior visual observation) |  |  |  |  |  |  |  |  |  |
|  | Trash, debris, sediment |  |  |  |  |  | Sump capacity between 50 and 75% full | Remove all floatables, debris, and sediment |  |
|  | (Note depth and determine %) |  |  |  |  |  |  |  |  |  |
|  | Floatables in weir box |  |  |  |  |  | Floatables layer is greater than 2" deep or | Remove the floatable layer more frequently if it |  |
|  | (Measure floatable depth) |  |  |  |  |  | interfering with normal operation of unit | accumulates more rapidly than settleable solids |  |
|  | Interior of CDS unit |  |  |  |  |  | Problems with the inlet flume, oil baffle, | Fix or replace any malfunctioning or defective |  |
|  | (Interior visual observation) |  |  |  |  |  | container cylinder, & separation chamber | components of the CDS Unit and contact Town |  |
|  | Separation Screen |  |  |  |  |  | Separation screen clogged with trash, | Power wash separation screen once per year or |  |
|  | (Interior visual observation) |  |  |  |  |  | debris, sediment, and/or floatables | when flow problems are reported/observed |  |
|  | Vector Access |  |  |  |  |  | Evidence of vectors entering CDS unit | Seal all opening with gaskets or temp. caulk and |  |
|  | (Exterior visual observation) |  |  |  |  |  | through openings and/or improper seals | notify the Town about observed evidence |  |
|  | Groundwater Seepage |  |  |  |  |  | Groundwater is observed entering into | Properly seal all cracks, holes, or breaks to |  |
|  | (Interior visual observation) |  |  |  |  |  | unit by way of cracks, holes, or breaks | prevent groundwater intrusion into CDS unit |  |
|  | Stormwater Discharges |  |  |  |  |  | Turbid water is observed discharging | Verify proper cleaning of unit and, if observed, |  |
|  | (Outlet visual observation) |  |  |  |  |  | from the CDS unit during storm events | contact Town about upstream pollutant sources |  |
|  | Other Inspection Items |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | SUMP CLEANING |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Record all of the following information only when performing maintenance activities on the CDS Unit | Date Performed: |  |  |
|  | Contractor Name: |  |  |  |  |  |  | Material Quantity: |  | cyds | Type of Equipment: |  |  |

All trash, debris, and sediment removed from the CDS Unit during the maintenance activities must be properly disposed of by the contractor

|  | Contractor Name: |  |  |  | Material Quantity: |  | cyds | Disposal Location: |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Signature of Qualified Inspector: |  | Date |  | Signature of Qualified Professional: |  | Date |

Last Revised: April 2009	page 1 of 2

TOWN OF BETHLEHEM - Continuous Deflective Separation (CDS) Unit Maintenance Inspection	PHOTO SHEET

Instructions: Use this sheet to attach files of photos taken during inspection of the CDS Unit – At a minimum, include the Diversion Weir, Separation Cylinder, Overflow Chamber, and Discharge Pipe. (Depending on the CDS Unit model being inspected, these parts may be in 1 or 2 precast MHs).

| PHOTO: DIVERSION WEIR FOR INSPECTED CDS UNIT | PHOTO: SEPARATION CYLINDER OF INSPECTED CDS UNIT |
| --- | --- |

| PHOTO: OVERFLOW CHAMBER FOR INSPECTED CDS UNIT | PHOTO: DISCHARGE PIPE FROM INSPECTED CDS UNIT |
| --- | --- |

Form available online at: www.townofbethlehem.org/pages/forms/showForms.asp#DPWEng	SUBMIT FORM BY E-MAIL	page 2 of 2